## Slide 1
ET AI HACKATHON 2026 · PROBLEM STATEMENT 2
AI-Driven Energy Supply Chain
Resilience for India
A live digital twin of India's crude-oil import network modeling chokepoint disruptions and recommending an adaptive procurement response in under a second.
71-node knowledge graph
2-stage stochastic LP + CVaR
4 disruption scenarios
111 automated tests
Prepared by DeadlineDriven · July 2026
Notes: Title. One line to open: this is a working prototype, not a mockup -- every number on the following slides comes from code that actually runs.

## Slide 2
THE PROBLEM
India's crude supply runs through a handful of contested chokepoints
India refines nearly 5 million barrels a day of crude it does not produce, and roughly half of it physically transits one strait. PS2 asks for an AI system that gives planners early warning of a disruption and models the best way to respond because when a chokepoint closes, the response window is days, not months.
4,936
kbpd of crude imported
(FY2025-26, PPAC-verified)
89.7%
of crude processed
is imported, not domestic
48.2%
of import capacity is
Hormuz-exposed (exposure-weighted)
~9.5 days
of cover from India's
5.33 MMT strategic reserve
!
This isn't a hypothetical stress-test. The Strait of Hormuz has been effectively closed to commercial shipping since 28 Feb 2026 and still is today (verified via live search, not training-data recall see slide 9). The scenario this build treats as its worst case is the real, ongoing situation.
02
Notes: Set the stakes with real PPAC numbers, then land the punch: the worst-case scenario in our demo is not invented -- it's the actual news as of the app's own 'today'.

## Slide 3
SCOPE
What we built, against PS2's five illustrative components
PS2 component | Status | What exists today
Supply Chain Digital Twin | Built | 71-node / 65-edge knowledge graph + 5-tab interactive dashboard, fully PPAC/DGCI&S sourced
Disruption Scenario Modeller | Built | 4 chokepoint scenarios (Hormuz 50%/100%, Red Sea/Suez 80%) degrade the live graph on demand
Adaptive Procurement Orchestrator | Built | Two-stage stochastic LP with CVaR risk-aversion, solved in under a second (Pyomo + HiGHS)
Geopolitical Risk Intelligence Agent | Scoped down | Curated real 2026 headlines drive signal extraction; not yet live multi-source monitoring
Strategic Reserve Optimisation Agent | Scoped down | SPR drawdown modeled per-scenario; single representative day, not a multi-day depletion schedule
Full detail on every scope cut is in Known Limitations (slide 11) disclosed deliberately, not discovered by a judge.
03
Notes: Walk the table top to bottom. Be upfront about the two 'scoped down' rows before a judge finds them -- it reads as maturity, not weakness.

## Slide 4
ARCHITECTURE
From source documents to a decision, in five layers
Source documents PPAC Ready Reckoner · PPAC Monthly Snapshot · ICB Notification · DGCI&S country-wise trade export
↓
build_network.py → Knowledge Graph (data/network.json) 71 nodes · 65 edges, typed & unit-tested
↓
↓
↓
Signal Extractor signal_extractor.py Real headline → severity + corridor signal
→
Scenario Engine scenario_engine.py Degrades edge capacity by chokepoint severity × exposure
→
Procurement Orchestrator optimizer.py 2-stage stochastic LP + CVaR (Pyomo / HiGHS), <1s solve
↓
briefing_generator.py translates optimizer output into plain-language cards, no jargon
↓
Streamlit App (app.py) 5-tab dashboard: Current System · Scenarios · News · Details & Charts · Data & Methods
↓
Decision-maker / Judge
04
Notes: This is the architecture diagram deliverable, folded into the deck. Point out that every box is a real file in the repo -- nothing here is aspirational.

## Slide 5
DATA FOUNDATION
A knowledge graph built on cited government data, not estimates
71
nodes
65
edges
16
refineries
(~97% of national
capacity)
37
supplier nodes
(33 countries +
4 domestic regions)
11 ports · 4 corridors · 3 SPR sites typed nodes, every one linked to a real coordinate and, where applicable, a PPAC table reference
Sourced from: PPAC Ready Reckoner FY25-26, PPAC Monthly Snapshot Jun'26, ICB Notification, DGCI&S country-wise crude import register (34 countries, calendar 2025).
Chart: Crude import share by supplier country FY2025-26 (DGCI&S-verified)
| Russia | Iraq | Saudi Arabia | UAE | USA | 28 other countries
Import share | 32.7 | 18.8 | 13.2 | 10.8 | 7.4 | 17.1
05
Notes: Every figure here traces to a cited PPAC table or the DGCI&S export -- this is the slide to point to if a judge asks 'is this data real or assumed'.

## Slide 6
SCENARIO MODELLING
Four disruption scenarios, weighted by planning probability
Each scenario degrades a chokepoint's shipping-route capacity by severity × that edge's chokepoint exposure a fraction, not a binary on/off, since not every barrel on a “Hormuz supplier” route physically transits the strait.
Baseline
No disruption
55%
planning probability
Hormuz 50%
Partial capacity loss
25%
planning probability
Red Sea / Suez 80%
Near-total suspension
15%
planning probability
Hormuz 100%
Full closure
5%
planning probability
Probabilities are illustrative planning assumptions, documented as such not a geopolitical forecast.
06
Notes: Explain exposure-weighting briefly -- it's what makes the Hormuz KPI on slide 9 land inside the real reported range instead of overstating it.

## Slide 7
ADAPTIVE PROCUREMENT ORCHESTRATOR
A risk-aware allocation problem, not a lookup table
1
Two-stage stochastic
Contracts are locked before the scenario is known (first-stage); flow, spot purchases, and SPR draw adapt per scenario (second-stage).
2
CVaR risk-aversion (λ)
A single slider trades expected cost against worst-case cost λ=0 is risk-neutral, higher λ protects the worst 5-10% of outcomes more.
3
Take-or-pay economics
70% of contracted volume is paid for even if a scenario can't deliver it mirrors real term-crude contracts, and is what makes over-committing to a fragile route genuinely costly.
4
Solved in production math
Pyomo + HiGHS, open-source, no commercial solver the full network solves in well under a second, live, behind an interactive slider.
Caught by its own test suite: an early build made every variable scenario-indexed with no shared first-stage decision, so λ produced a byte-identical solution. Fixed and kept as a regression test see slide 10.
07
Notes: The take-or-pay point is the one that shows real domain modeling, not just LP boilerplate -- worth slowing down on.

## Slide 8
THE DIGITAL TWIN, IN USE
One dashboard, five tabs, zero jargon until you ask for it
1
Current System
Plain-English explanation, baseline stat cards, and the live import map.
2
Scenarios
Pick a disruption via clickable pill-cards; get the plain-language story and an updated map no charts, no jargon.
3
News
Same story, triggered by a real dated headline instead of a manual pick.
4
Details & Charts
Full technical home: KPIs, the technical briefing, cost/shift/refinery charts, and a 4-slider robustness stress-test.
5
Data & Methods
Sources, assumptions, node/edge tables, PPAC-verified figures, and the real-world validation comparison (slide 9).
08
Notes: Screen-record each tab in this order for the demo video -- it matches the script.

## Slide 9
VALIDATION
Checked against the real, ongoing Hormuz crisis not a synthetic test
Metric | This model | Real-world reported
Hormuz-routed import share | 48.2% (exposure-weighted) | 40–52% (multiple sources)
Capacity lost under full closure | 48.2% (2,380 of 4,936 kbpd) | “over 40%” of crude flows (OilPrice.com)
Strategic reserve cover | 5.33 MMT, ~9.5 days at full fill | 5.33 MMT, “9-10 days of cover” (independent report)
Diversification direction | Risk-averse plan shifts contracts away from Hormuz-exposed suppliers | India secured ~70% of imports outside Hormuz by 11 Mar 2026 (Petroleum Ministry)
What this doesn't capture: the IEA's coordinated 400M-barrel strategic release, GDP/rupee/capital-flow effects, price-controlled retail fuel losses to Indian oil marketing companies, and the human cost of the underlying conflict. This model gets the supply network arithmetic right and says plainly what it doesn't model.
09
Notes: This is the credibility slide. Checked via live web search dated 21 July 2026 (postdates any static training cutoff) -- full citations in KNOWN_LIMITATIONS.md section 8.

## Slide 10
ENGINEERING RIGOR
We test the math, not just the UI
111
automated tests
across 8 test files
3
high-severity modeling
bugs found by audit
all fixed & re-tested
0
integer/binary
variables a clean LP,
sub-second solve
AppTest
end-to-end UI tests, not
just unit tests on the math
An independent audit found and we fixed:
✓
Domestic supply stranded at ports
~450 kbpd of real indigenous crude could reach a port but had no onward edge invisible to the optimizer. Fixed: ports now route indigenous flow onward.
✓
SPR drained on an ordinary day
The reserve was priced cheaper than routine spot crude with no depletion cost, so the model used it as a free daily supplier. Fixed: baseline no longer draws the reserve.
✓
Domestic production caps missing
Regions could be drawn 2-3x their real output because only pipeline capacity, not field production, was enforced. Fixed: production caps are now a real constraint.
10
Notes: Frame this as a strength, not a confession: we ran an adversarial audit against our own solved model, found real bugs, fixed them, and kept regression tests so they can't come back silently.

## Slide 11
KNOWN LIMITATIONS
What we are not claiming disclosed, not discovered
i
Single-period model
One representative day per scenario no multi-day SPR depletion or replenishment schedule.
i
No rerouting-with-delay
alt_corridor / alt_transit_days are recorded on every edge but not yet consumed by the optimizer.
i
No disruption-time freight spike
Freight/insurance cost is static; real chokepoint crises raise it 15-40% on affected routes.
i
Fairness objective cut
CVaR redistributes shortfall pain across refineries; it doesn't guarantee an equitable minimum service level.
i
Grade-compatibility constraint
Our own spec calls for it; grade/grade_preference data exists but isn't yet enforced in the solver.
i
SPR figures via PIB/Wikipedia
Not independently verifiable against PPAC's Ready Reckoner SPR sits under a separate ministry program.
Every item above is a deliberate scope cut, documented in KNOWN_LIMITATIONS.md before any judge could ask about it none of them changes what the demo shows.
11
Notes: If asked about any one of these in Q&A: 'yes, documented, here's why it doesn't affect what we're demonstrating' -- not a scramble.

## Slide 12
FUTURE PLANS
What we'd build next, in priority order
1
Multi-day SPR dynamics
Turn the single “day 1” snapshot into a real depletion-and-replenishment schedule across the response window.
2
Rerouting-with-delay
Consume the alt_corridor / alt_transit_days data that already exists let the optimizer choose a slower, safer path instead of only reallocating volume.
3
Grade-compatibility constraint
Close the one gap against our own model spec: stop the solver from assigning crude a refinery can't actually process.
4
Live signal ingestion
Replace curated headlines with real RSS/news-API monitoring, and layer in AIS vessel tracking where available.
5
Fairness objective
Add the cited but unbuilt equitable-service-level term so shortfall isn't just minimized, but distributed fairly across refiners.
6
True multi-agent reasoning
Let an LLM reason over the knowledge graph and propose actions, rather than templating the optimizer's output today's pipeline is agent-flavored, not yet agentic.
12
Notes: Order matters here -- SPR dynamics and grade-compatibility are the cheapest, most defensible next steps; multi-agent reasoning is the most ambitious and should be framed as a direction, not a promise.

## Slide 13
DELIVERABLES
Everything PS2 asked for
✓
Working Prototype
Streamlit app, live every number traceable to code.
✓
Architecture Diagram
Slide 4 of this deck.
✓
Presentation Deck
This document.
✓
Demo Video
3-4 minute walkthrough, script prepared.
Digital Twin · Adaptive Procurement Orchestrator · Disruption Scenario Modeller
Built on cited PPAC and DGCI&S government data, stress-tested against the real, ongoing Hormuz crisis, and audited for the kind of bugs a demo would never surface on its own.
Thank you
DeadlineDriven · ET AI Hackathon 2026 · PS2
13
Notes: Close on the checklist -- it directly answers the hackathon's own 'expected deliverables' list, which is worth saying out loud to the judges.